## Slide 1: Collective-Capable AXI4 NoC Target Specification
Revision 0.2, 2026-07-23, draft

## Slide 2: MHA dataflow requirements for the NoC
MHA dataflow demand
  High bandwidth : Q, K, V multicast, activations, KV cache blocks
    Burst-based
  Latency sensitive : Softmax statistics, synchronization, scheduler start and done
    Single-beat messages
  Control message: Requests, acknowledgments
    Small fixed-size flits
NoC design goal
  Traffic-class isolation
    High Bandwidth traffic
    Latency-sensitive traffic
  Collective-Capable NoC for Large-Scale Accelerators
  Multiple flexible configuration options

## Slide 3: Key features
512 b data, 64 GB/s @ 1 GHz
Header overhead 7 %
Three physical networks REQ / RSP / DAT
REQ/RSP full-duplex W/R utilization 81.4 % on DAT
Support AXI Outstanding / Interleaving / Out-of-Order
2x2 to 16x16 mesh, 256 nodes
Write multicast / Response reduction support
1 to 8 virtual channels, credit-based on DAT, ready/valid on REQ / RSP
XY wormhole, deadlock-free
GALS, per-endpoint clocks

## Slide 4: How to handle heterogeneous traffic
High Bandwidth traffic
DMA traffic
Wide busses (512-bit)
Burst-based
Large messages (few kBs)
Latency tolerant
Latency-sensitive traffic
Core traffic
Synchronization
Single-word messages
Control traffic traffic
Request messages
Acknowledgment messages (AXI write responses)
Small messages
Wide links
with high utilization
Narrow links with
low utilization
Wide
Req
Rsp
Wide
Req

## Slide 5: AXI to Physical link mapping
 |  | Mapping & primary payload | 
Physical link | Size | Narrow class | Data class
REQ | 137b | AW, AR: 48 b address W: 64 b data | AR: 48 b address
RSP | 127b | R: 64 b data B: 2 b response | B: 2 b response
DAT | 629b | - | AW: 48 b address W, R: 512 b data
AXI4 requests and responses are always transmitted over separate physical links to avoid message-level deadlocks. The REQ and RSP links are mainly used to handle latency-sensitive requests and responses from compute cores.
REQ/RSP links are utilized for read requests and write responses from the wide AXI4 bus, as these messages do not fully utilize the bandwidth of a wide link. By mapping them to narrow links, the wide link is reserved for high-bandwidth traffic, such as read and write bursts.

## Slide 6: NMU (Network Master Unit)
Request path
  Round-robin arbitration with wormhole lock
  SAM(System Address Map)
    Global Address Translate to Local Address
Response path
  Reorder buffer: 8 KB SRAM, two responses at the AXI 4 KB maximum burst
    Same-ID ordering: same-destination streams bypass the reorder buffer

## Slide 7: NSU (Network Slave Unit)
Request path
  Packet buffer
  ID compression: narrower downstream ID width
    Streams sharing a compressed ID return in order
Response path
  Header FIFO: header kept for response packetization

## Slide 8: Architecture
Each node holds one compute tile and its local memory, so it is both an AXI master and an AXI slave
XY routing fixes the path a multicast takes, its merged response retraces that path in reverse

## Slide 9: NI & Router Interfaces
Unit | AXI interface | NoC interface
NMU | AXI slave interface | NoC initiator interface
NSU | AXI master interface | NoC target interface
Router | - | NoC link interface per port, one local and four directional (N, E, S, W)

## Slide 10: AXI channel signals
One AXI4 channel set for NMU and NSU, widths per the spec.
Channel | Signals | Key widths
Write address AW | AWID, AWADDR, AWLEN, AWSIZE, AWBURST, AWLOCK, AWCACHE, AWPROT, AWQOS, AWREGION, AWUSER, AWVALID, AWREADY | AWADDR 48, AWID 8, AWUSER 58
Write data W | WDATA, WSTRB, WLAST, WUSER, WVALID, WREADY | WDATA 64 or 512, WSTRB 8 or 64
Write response B | BID, BRESP, BUSER, BVALID, BREADY | BID 8, BRESP 2, BUSER 8
Read address AR | ARID, ARADDR, ARLEN, ARSIZE, ARBURST, ARLOCK, ARCACHE, ARPROT, ARQOS, ARREGION, ARUSER, ARVALID, ARREADY | ARADDR 48, ARID 8, ARUSER 8
Read data R | RID, RDATA, RRESP, RLAST, RUSER, RVALID, RREADY | RDATA 64 or 512, RRESP 2

## Slide 11: NoC link interface
Network | Flit width | Flow control
REQ | 137 | valid and ready, one instance per direction
RSP | 127 | valid and ready, one instance per direction
DAT | 629 | valid plus per-virtual-channel credit return, no ready
Each link carries the three physical networks, each an independent signal group per direction

## Slide 12: NoC Communication Protocol – Flit header
Field | Bits | Width | Description
axi_ch | [3:0] | 4 | AXI channel of the flit. 0: NarrowAw, on REQ 1: NarrowW, on REQ 2: NarrowAr, on REQ 3: NarrowB, on RSP 4: NarrowR, on RSP 5: DataAw, on DAT 6: DataW, on DAT 7: DataAr, on REQ 8: DataB, on RSP 9: DataR, on DAT
src_id | [11:4] | 8 | Source node id, composed as {y[3:0], x[3:0]}
dst_id | [19:12] | 8 | Destination node id, same composition
fixed_vc | [20] | 1 | Holds vc_id end to end, no per-hop reallocation.
vc_id | [23:21] | 3 | Virtual channel index, 0 to the configured VC count minus one
flit_tail | [24] | 1 | Indicates the last flit of a packet
ordering_req | [25] | 1 | When asserted, ordering_tag is valid
ordering_tag | [33:26] | 8 | Reorder slot handle, allocated per transaction. Bounds a master to 256 outstanding transactions
collective_op | [35:34] | 2 | Collective operation. 0: UNICAST, single destination, collective_mask zero 1: MULTICAST, replicate a request to the node set of collective_mask, merge its responses, error BRESP first 2-3: reserved Write path only
collective_mask | [43:36] | 8 | Derived from the AWUSER address mask

## Slide 13
Flit payload, requests and write data
Aw, Ar, 93 b | Bits | Width
id | [7:0] | 8
addr | [55:8] | 48
len | [63:56] | 8
size | [66:64] | 3
burst | [68:67] | 2
cache | [72:69] | 4
lock | [73] | 1
prot | [76:74] | 3
region | [80:77] | 4
qos | [84:81] | 4
user | [92:85] | 8
NarrowW, 81 b | Bits | Width
last | [0] | 1
user | [8:1] | 8
strb | [16:9] | 8
data | [80:17] | 64
DataW, 585 b | Bits | Width
last | [0] | 1
user | [8:1] | 8
strb | [72:9] | 64
data | [584:73] | 512

## Slide 14
Flit payload, responses and AWUSER
NarrowR, 83 b | Bits | Width
last | [0] | 1
id | [8:1] | 8
resp | [10:9] | 2
user | [18:11] | 8
data | [82:19] | 64
DataR, 531 b | Bits | Width
last | [0] | 1
id | [8:1] | 8
resp | [10:9] | 2
user | [18:11] | 8
data | [530:19] | 512
AWUSER, 58 b | Bits | Width
user | [7:0] | 8
collective_op | [9:8] | 2
collective_mask | [57:10] | 48
B, 18 b | Bits | Width
id | [7:0] | 8
resp | [9:8] | 2
user | [17:10] | 8

## Slide 15: Header overhead and W/R utilization
Header overhead counts the 44 b header over the flit width. W and R utilization count the AXI data field over the flit width.
Data utilization counts the AXI data field alone.
DataAw rides DAT for ordering, not size: AXI4 write data carries no ID, a slave pairs data with requests by arrival order, so the request travels bundled ahead of its data. The cost is one flit per write burst and amortizes over the burst length.
Network | Header overhead | W utilization | R utilization
REQ 137 b | 32.1 % | 46.7 %, NarrowW | -
RSP 127 b | 34.6 % | - | 50.4 %, NarrowR
DAT 629 b | 7.0 % | 81.4 %, DataW | 81.4 %, DataR

## Slide 16: Configuration options
Feature | Parameter | Values (default) | Comments
Topology | Mesh X and Y dimension | 2-16 (4) | Square meshes only. 256 nodes maximum, set by the 8-bit node ID
AXI interface | Endpoint interfaces | 1, 2 (1) | One interface carries both classes, with the class selected by the SAM address space. Two carry one class each
Flow control | NUM_VC, virtual channels per network channel | 1-8 (1) | Sets the NoC link interface credit signal width
Ordering | Outstanding depth | 1-32 (32) | 1 when same-ID response reordering is disabled. A master holds at most 256 in total, one per ordering_tag, see section 6
Ordering | Re-order buffer | 0,1(1) | The ordering requirement holds in either setting
Address map | SAM address spaces | config, memory | Config space selects the narrow class, memory space the data class. Uniform across nodes, loaded at runtime

## Slide 17: Metrics
Metric | Definition
Payload bandwidth | AXI payload the same link carries, data width x clock / 8
Payload efficiency | Data beats over flits carried
Zero-load latency | Packet latency with no queueing and no contention
Sustained bandwidth | Payload bandwidth a channel delivers over a continuous stream
All figures assume AXI and NoC on one 1 GHz clock, the 512 b data class, and 4 KB bursts.

## Slide 18: Payload bandwidth
A physical network carries one flit per cycle per direction and a flit holds at most one beat of AXI payload.
AXI interface, per port
  Narrow W, R: 64 b @ 1 GHz = 8 GB/s each
  Data W, R: 512 b @ 1 GHz = 64 GB/s each
NoC channel, per link direction
  REQ: flit 137 b @ 1 GHz = 17.1 GB/s channel, 8 GB/s payload
  RSP: flit 127 b @ 1 GHz = 15.9 GB/s channel, 8 GB/s payload
  DAT: flit 629 b @ 1 GHz = 78.6 GB/s channel, 64 GB/s payload

## Slide 19: Payload efficiency
Write
  Shares DAT with AW+W
  One flit per burst
  N/(N+1) payload efficiency
Read
  Response-direction DAT to itself
  No flit shared
  100% payload efficiency
Burst length | Payload efficiency
1 beat (64 B) | 50%
4 beats | 80%
16 beats | 94.1%
64 beats (4 KB) | 98.5%
The bandwidth problem with serialization

## Slide 20: Sustained bandwidth: full rate unless reads reorder
In-order reads hold the full rate, 64 GB/s.
Out-of-order reads lift efficiency across destinations, but the reorder-buffer size is their bottleneck
  every reordered response passes through it, and once its 8 KB is fully allocated the next request waits.
Burst size | Outstanding | Pending data (B) | Coverage (cycles) (pending data / 64 B per cycle)
64B | 32 | 2048 | 32
256B | 32 | 8192 | 128
1024B | 8 | 8192 | 128
4096B | 2 | 8192 | 128

## Slide 21: Zero-load latency
A packet crossing H hops traverses H links and passes H + 1 routers, counting the source router.
  REQ / RSP: simple-mode router, ready/valid, 1 to 2 pipeline stages per hop
  DAT: standard-mode router, multi-VC credit-based flow control, 3 to 5 pipeline stages per hop

## Slide 22: Evaluation Model
The evaluation platform is the Edge LPDDR PIM 3D scalable architecture. The NoC under test is the router mesh and network interfaces of its NPU mesh region.
Host control region: a scheduler CPU and a sequencer DMA stage data from LPDDR and external storage into the mesh
NPU mesh region: one tile per node. A tile holds an NPU, its controller, tile-local 3D DRAM, and a router

## Slide 23: Memory tiers, cold storage to compute
Tier | Location | Role
External storage | Host control region, loaded from Flash | Persistent model store, read once at model load
LPDDR | External DRAM behind the LPDDR interface | Capacity tier. Holds the model image and feeds weight staging
Host 3D DRAM | Host control region | Bandwidth tier on the host side. KV cache offload target and sink of mesh output
Interface buffer | Host control region | Staging buffer between the external interfaces and the sequencer DMA
Local SRAM | Host control region | Scheduler working memory, holds DMA descriptors
Tile 3D DRAM | Every mesh tile | Near-memory tier. Resident weights, the tile's Q, K, V, O blocks, and hot KV cache. Tile-local, so a source-tile load generates no NoC traffic
L1 | Inside the NPU | Compute scratchpad. Sub-tiles, partial sums, and online-softmax state, filled by tiling with double buffering

## Slide 24: Tiled attention dataflow
Three algorithms specify the dataflow: model-level execution flow at the run level, and the attention block it invokes as per-tile fetch or multicast, differing only in how shared operands reach the tile group.
Attention block mapping
A tile group computes one attention block: the score grid S = Q K^T maps onto the mesh, rows share Q, columns share K/V
Attention block mapping onto a 4 x 4 tile group

## Slide 25: Model-level execution flow
Weights load once into per-tile 3D DRAM and stay resident, no layer fetches weights over the fabric. A layer puts two traffic classes on the fabric:
Feature pipeline: activations passed to the next layer, on the data plane.
Scheduler control: per-group start and done messages, on the narrow control plane.
Layers map to tile groups round-robin as pipeline stages. A group holds the weights and KV cache of its layers, so only the activations X cross group boundaries:

## Slide 26: Algorithms 1 and 2
Algorithms 1 and 2 differ in one place, how a shared slice reaches its consumers:
Algorithm 1 (per-tile fetch): every consumer tile pulls the slice itself, Gx unicast reads per Q slice and Gy per K/V slice (lines 5 and 7)
Algorithm 2 (multicast): the source tile reads its slice locally once and multicasts it, one transfer per slice (lines 5-6 and 8-9)
In both figures the comments mark plane use: data for the Q, K, V, O tensors, narrow for the m and l statistics, local read/write for 3D DRAM accesses that generate no NoC traffic.

## Slide 27: Algorithm 1 Per-tile fetch
Every consumer tile pulls the slice itself, Gx unicast reads per Q slice and Gy per K/V slice.

## Slide 28: Algorithm 2 Multicast
Algorithm 2: multicast on a Gx x Gy tile group
The source tile reads its slice locally once and multicasts it, one transfer per slice.

## Slide 29: Multicast model and tail latency
The row and column multicasts of Algorithm 2 follow the model below, a multicast along one axis over a set of k nodes. A submesh multicast runs in two phases, one per axis.
Case | Tail arrival at the farthest member
Repeated unicast | (k - 1)L + H_max t_wire + (H_max + 1) t_router
In-network multicast | L + H_max t_wire + (H_max + 1) t_router